# 3-row P2 or P3 connector map to one S-LINK LSC 
using P2-type backplane

|  |  | A | B | C |
| --- | --- | --- | --- | --- |
|  | 1 | DL1 (2) | Vcc (1) | DL0 (2) |
|  | 2 | DL3 (2) | Gnd (1) | DL2 (2) |
|  | 3 | Gnd (3) | BL0 (1) | DL4 (2) |
|  | 4 | UD0 | BL1 (1) | Gnd (3) |
|  | 5 | UD2 | BL2 (1) | UD1 |
|  | 6 | UD4 | BL3 (1) | UD3 |
|  | 7 | UD6 | BL4 (1) | UD5 |
|  | 8 | Gnd (3) | BL5 (1) | UD7 |
|  | 9 | UD8 | BL6 (1) | Gnd (3) |
|  | 10 | UD10 | BL7 (1) | UD9 |
|  | 11 | UD12 | BL8 (1) | UD11 |
|  | 12 | UD14 | Gnd (1) | UD13 |
|  | 13 | Gnd (3) | Vcc (1) | UD15 |
|  | 14 | UD17 | BL9 (1) | UD16 |
| LSC | 15 | UD18 | BL10 (1) | Gnd (3) |
| SLOT | 16 | UD20 | BL11 (1) | UD19 |
| C | 17 | UD22 | BL12 (1) | UD21 |
|  | 18 | Gnd (3) | BL13 (1) | UD23 |
|  | 19 | UD25 | BL14 (1) | UD24 |
|  | 20 | UD26 | BL15 (1) | Gnd (3) |
|  | 21 | UD28 | BL16 (1) | UD27 |
|  | 22 | UD30 | Gnd (1) | UD29 |
|  | 23 | Gnd (3) | BL17 (1) | UD31 |
|  | 24 | UCTRL# | BL18 (1) | UDW0 |
|  | 25 | UDW1 | BL19 (1) | UTEST# |
|  | 26 | URESET# | BL20 (1) | Gnd (3) |
|  | 27 | Gnd (3) | BL21 (1) | UWEN# |
|  | 28 | UCLK | BL22 (1) | Gnd (3) |
|  | 29 | Gnd (3) | BL23 (1) | LFF# |
|  | 30 | LDOWN # | BL24 (1) | NC (4) |
|  | 31 | LRL0 | Gnd (1) | LRL1 |
|  | 32 | LRL2 | Vcc (1) | LRL3 |

BLx (1)	: Bused Line, user definable signal bused between slots

Gnd (1)	: Ground from backplane

Vcc (1)	: +5 Volt power supply from backplane

DLx (2)	: Direct Line, user definable signal with direct connection from front side to rear side

Gnd (3)	: Ground, connect to groundplane and to Gnd pins from row B on both front module

and on rear module

NC (4)	: Do not connect (corresponds to LDERR# line on LDC connector)

# 3-row P2 or P3 connector map to one S-LINK LDC 
using P2-type backplane

|  |  | A | B | C |
| --- | --- | --- | --- | --- |
|  | 1 | DL1 (2) | Vcc (1) | DL0 (2) |
|  | 2 | DL3 (2) | Gnd (1) | DL2 (2) |
|  | 3 | Gnd (3) | BL0 (1) | DL4 (2) |
|  | 4 | LD0 | BL1 (1) | Gnd (3) |
|  | 5 | LD2 | BL2 (1) | LD1 |
|  | 6 | LD4 | BL3 (1) | LD3 |
|  | 7 | LD6 | BL4 (1) | LD5 |
|  | 8 | Gnd (3) | BL5 (1) | LD7 |
|  | 9 | LD8 | BL6 (1) | Gnd (3) |
|  | 10 | LD10 | BL7 (1) | LD9 |
|  | 11 | LD12 | BL8 (1) | LD11 |
|  | 12 | LD14 | Gnd (1) | LD13 |
|  | 13 | Gnd (3) | Vcc (1) | LD15 |
|  | 14 | LD17 | BL9 (1) | LD16 |
| LDC | 15 | LD18 | BL10 (1) | Gnd (3) |
| SLOT | 16 | LD20 | BL11 (1) | LD19 |
| C | 17 | LD22 | BL12 (1) | LD21 |
|  | 18 | Gnd (3) | BL13 (1) | LD23 |
|  | 19 | LD25 | BL14 (1) | LD24 |
|  | 20 | LD26 | BL15 (1) | Gnd (3) |
|  | 21 | LD28 | BL16 (1) | LD27 |
|  | 22 | LD30 | Gnd (1) | LD29 |
|  | 23 | Gnd (3) | BL17 (1) | LD31 |
|  | 24 | LCTRL# | BL18 (1) | UDW0 |
|  | 25 | UDW1 | BL19 (1) | UTDO# |
|  | 26 | URESET# | BL20 (1) | Gnd (3) |
|  | 27 | Gnd (3) | BL21 (1) | LWEN# |
|  | 28 | LCLK | BL22 (1) | Gnd (3) |
|  | 29 | Gnd (3) | BL23 (1) | UXOFF# |
|  | 30 | LDOWN # | BL24 (1) | LDERR # |
|  | 31 | URL0 | Gnd (1) | URL1 |
|  | 32 | URL2 | Vcc (1) | URL3 |

BLx (1)	: Bused Line, user definable signal bused between slots

Gnd (1)	: Ground from backplane

Vcc (1)	: +5 Volt power supply from backplane

DLx (2)	: Direct Line, user definable signal with direct connection from front side to rear side

Gnd (3)	: Ground, connect to groundplane and to Gnd pins from row B on both front module

and on rear module

# 5-row P2 or P3 connector map to two S-LINK LDCs
using P2-type VME64x backplane

|  |  | Z | A | B | C | D |
| --- | --- | --- | --- | --- | --- | --- |
|  | 1 | LD1 | DL1 (2) | Vcc (1) | DL0 (2) | LD0 |
|  | 2 | Gnd (1) | DL3 (2) | Gnd (1) | DL2 (2) | LD2 |
|  | 3 | LD4 | Gnd (3) | BL0 (1) | DL4 (2) | LD3 |
|  | 4 | Gnd (1) | LD0 | BL1 (1) | Gnd (3) | LD5 |
| Rows | 5 | LD7 | LD2 | BL2 (1) | LD1 | LD6 |
| A & C | 6 | Gnd (1) | LD4 | BL3 (1) | LD3 | LD8 |
| LDC1 | 7 | LD10 | LD6 | BL4 (1) | LD5 | LD9 |
|  | 8 | Gnd (1) | Gnd (3) | BL5 (1) | LD7 | LD11 |
|  | 9 | LD13 | LD8 | BL6 (1) | Gnd (3) | LD12 |
| Rows | 10 | Gnd (1) | LD10 | BL7 (1) | LD9 | LD14 |
| Z & D | 11 | LD16 | LD12 | BL8 (1) | LD11 | LD15 |
| LDC2 | 12 | Gnd (1) | LD14 | Gnd (1) | LD13 | LD17 |
|  | 13 | LD19 | Gnd (3) | Vcc (1) | LD15 | LD18 |
|  | 14 | Gnd (1) | LD17 | BL9 (1) | LD16 | LD20 |
|  | 15 | LD22 | LD18 | BL10 (1) | Gnd (3) | LD21 |
|  | 16 | Gnd (1) | LD20 | BL11 (1) | LD19 | LD23 |
|  | 17 | LD25 | LD22 | BL12 (1) | LD21 | LD24 |
|  | 18 | Gnd (1) | Gnd (3) | BL13 (1) | LD23 | LD26 |
|  | 19 | LD28 | LD25 | BL14 (1) | LD24 | LD27 |
|  | 20 | Gnd (1) | LD26 | BL15 (1) | Gnd (3) | LD29 |
|  | 21 | LD31 | LD28 | BL16 (1) | LD27 | LD30 |
|  | 22 | Gnd (1) | LD30 | Gnd (1) | LD29 | UDW0 |
|  | 23 | LCTRL# | Gnd (3) | BL17 (1) | LD31 | UDW1 |
|  | 24 | Gnd (1) | LCTRL# | BL18 (1) | UDW0 | UTDO# |
|  | 25 | LWEN# | UDW1 | BL19 (1) | UTDO# | URESET# |
|  | 26 | Gnd (1) | URESET# | BL20 (1) | Gnd (3) | UXOFF# |
|  | 27 | LCLK | Gnd (3) | BL21 (1) | LWEN# | URL0 |
|  | 28 | Gnd (1) | LCLK | BL22 (1) | Gnd (3) | URL1 |
|  | 29 | LDOWN # | Gnd (3) | BL23 (1) | UXOFF# | URL2 |
|  | 30 | Gnd (1) | LDOWN # | BL24 (1) | LDERR # | URL3 |
|  | 31 | LDERR # | URL0 | Gnd (1) | URL1 | Gnd (1) |
|  | 32 | Gnd (1) | URL2 | Vcc (1) | URL3 | Vcc (1) |

BLx (1)	: Bused Line, user definable signal bused between slots

Gnd (1)	: Ground from backplane

Vcc (1)	: +5 Volt power supply from backplane

DLx (2)	: Direct Line, user definable signal with direct connection from front side to rear side

Gnd (3)	: Ground, connect to groundplane and to Gnd pins from row B on both front module

and on rear module